## Slide 1: Segmenting C. ElegAns
Valerie Simonis
CSC 481: Final Project
11/18/2013

## Slide 2: Outline
Motivation / Problem Statement
Related Work
Methodology
  Data
  Approach
Results
  Demo Matlab GUI
Evaluation
    Demo Matlab GUI
References

## Slide 3: Motivation
Results of segmentation used in two applications:
  Track worms during video collection
    Centroid approximations to move X-Y stage
  Collect features to describe worm’s behavior
    Morphology: area, length
    Posture: curled, coiled, sinusoidal, …
    Movement: crawling, turning, …
What sequence of image processing techniques should I apply to adequately segment C. elegans from its environment ?
Worm Video
Segmented Worm
Worm Tracking
Feature Collection

## Slide 4: Related Work
Segmentation is a common problem to any worm tracking or worm analysis application
In general, the algorithm used is dependent on the set of images on which analysis is to be done, resulting in different groups creating algorithms based on image acquisition:
    “Histogram” approach (Yemini et al, 2012)
    Using reference background value and apply window at all pixel locations to filter it out (Baek et al, 2002)
Using thresholding and morphological closing is standard approach
Hard to tell from literature how adequate algorithms are as it is not usually a focal point of papers

## Slide 5: Methodology
Data and Approach

## Slide 6: DAta
Dr. Hongkyun Kim at Roslind Franklin University
Resolution: 1024 x 768
Number of frames: 300
Number of independent sequences (between stage movements):19
Select 5 representative images from the set to test segmentation

## Slide 7: Image Processing Sequence
Original Image
Image Enhancement
Thresholding
Morphological Operations
Segmented
Image
Histogram equalization
Contrast Stretching
Mean pixel value
Otsu
Histogram
Area Under Histogram
Opening
Closing
Connected Components

## Slide 8: Threshold Descriptions
  Find max = I(x,y) such that histogram is maximal
  Find T = I(x,y) such that T is the nearest minimum to the left of max
  Find T = I(x,y) such that the number of pixels in area to the left of T approximates the average area of a worm (4223)
worm
background
# of pixels
==
avg area of worm
T = 78
“Area Under Histogram”
“Histogram”
max
Nearest min to the left
worm
background
T = 86

## Slide 9: Results
Demonstration

## Slide 10: ‘nematodes’ GUI: Algorithm builder/Tester
Notes: medix-5.cstcis.cti.depaul.edu

## Slide 11: Demo: medix-5.cstcis.depaul.edu
Data
  Show each image & explain issue
Thresholds
  “First Frame”
    Mean Pixel Value
    Otsu
    Histogram
    Area under histogram
  “Intersect Artifact”
    Contrast Enhancement
    Area under histogram
    Morphology medium

## Slide 12: Evaluation

## Slide 13: Hand segmentation
Zoom in to maximum possible and overlay pixels on image
Difficult!

## Slide 14: Evaluation Methods
The GUI provides me with four methods of evaluation:
  One image:
    Visual Evaluation:
      Check skeleton, perimeter and centroid of segmentation
      Check skeleton and perimeter of hand drawn segmentation
    Numerical Evaluation:
  All images in a subset:
    Paired t-test:
    P-value:
      < 0.05: Reject null hypothesis ---> bad
      > 0.05: Fail to reject null hypothesis ---> good

## Slide 15: Conclusions
Best Configuration: Area Under Histogram with morphological closing
  First Frame: 91.5%
  Curled: 96.1 %
  Coiled: 97.1 %
  Artifact: 86.9 %
  Intersect Artifact: 101.7 %
  P-value: 0.1
  Visual check pretty good
Many improvements possible based on GUI results:
  Select connected component approximately “worm-sized”
  Split artifacts and remove them

## Slide 16: References
Baek, J-H, Cosman, P. , Feng, Z., Silver J., William R. Schafer, W.R. (2002). Using machine vision to analyze and classify Caenorhabditis elegans behavioral phenotypes quantitatively. Journal of Neuroscience Methods. 118:9-21.
Cohen, E., Yemini, E, Schafer, W., Feiterlson D.G., Treinin, M. (2012). Locomotion analysis identifies roles of mechanosensory neurons in governing locomotion dynamics of C. elegans. Journal of Experimental Biology. 215:3639-48.
Wu, Q., Merchant, F.A., Castleman, K.R. (2008). Microscope Image Processing. Academic Press.
Gonzalez, R.C., Woods, R.E. (2008). Digital Image Processing, Third Edition.Pearson Prentice Hall.
MathWorks, (2012). Examples: Program GUI Components (R2013b). Retrieved November 18, 2013 from http://www.mathworks.com/help/matlab/creating_guis/examples-programming-gui-components.html